## Slide 1: Marginal Cost of Road Transport Conceptual Framework and Implication for Bangkok
ATRANS Research Project the 5th ATRANS Symposium
24 August 2012

## Slide 2: Background
Transport creates both benefits and costs.
One of the key principles in transportation economics: making road users pay for the external costs they cause.
European countries: issue of marginal cost pricing
Thailand: road transport users are heavily subsidized by the government budget, with only few toll roads.
Question that arises:
Do the road users in Thailand pay more or less on what they impose to the society at large?

## Slide 3: Research Objectives
To review the concept of marginal cost of road transport including the external costs.
To define the categories of costs and revenues of road transport in Thailand.
To compare the marginal costs and the price that road users pay.
To recommend a measure for efficient pricing mechanism.

## Slide 4: Marginal Costs and Revenues Categories
Category | Marginal Cost Basis
Cost of capital | Not relevant
Infrastructure costs | Mainly wear & tear costs that can be related to increase vehicle km.
Vehicle operating costs (public transport) | Cost of an additional vehicle km.
Congestion | Costs imposed by one user on all other users of the transport system.
Scarcity | Opportunity cost of providing a service that precludes other services being run.
Mohring effect | Benefits of increased service frequencies due to additional vehicle km.
Accidents | External costs of an additional vehicle km, including the increase/decrease in accident risk due to increased traffic.
Environmental costs | Cost of an additional vehicle km
Fuel duties | Revenue associated with an additional vehicle km
Vehicle excise duty | Revenue relating to an additional vehicle km – only for those vehicles where an increase in vkm would result in an expansion of vehicle fleet (e.g. HGVs, PSVs, but not cars, LDVs).
Value added tax | On fuel duties
Fares, freight tariffs | Associated with an additional vehicle km

## Slide 5: Research Framework

## Slide 6
Traffic Volume Result
 | 2011 | 2010 | 2009 | 2008 | 2007
CAR | 93,808 | 85,395 | 79,752 | 75,331 | 71,918
Pick Up | 32,640 | 31,476 | 31,397 | 31,350 | 31,352
Motorcycle | 9,994 | 9,471 | 9,163 | 8,926 | 8,653
TAXI | 10,523 | 10,104 | 9,407 | 8,795 | 8,345
Motorcycle Taxi | 2,457 | 2,568 | 2,889 | 3,014 | 3,053
BUS | 2,525 | 2,418 | 2,227 | 2,114 | 2,048
TRUCK | 6,358 | 5,959 | 6,310 | 6,346 | 6,195
Total | 158,306 | 147,391 | 141,145 | 135,876 | 131,564
Unit: million vehicle-km.

## Slide 7
Traffic Volume Result
2011
 | Benzene | Diesel | LPG | CNG
CAR | 67.04% | 16.48% | 14.03% | 2.45%
Pick Up | 3.32% | 91.77% | 3.47% | 1.45%
Motorcycle | 100.00% | 0.00% | 0.00% | 0.00%
TAXI | 1.58% | 0.00% | 38.63% | 59.79%
Motorcycle Taxi | 100.00% | 0.00% | 0.00% | 0.00%
BUS | 0.00% | 58.09% | 2.24% | 39.67%
TRUCK | 0.00% | 95.42% | 0.00% | 4.58%

## Slide 8: Infrastructure Cost Estimated for Bangkok
 | Department of Highways (Million Baht) | Department of Rural Highways (Million Baht) | Bangkok Metropolitan Administration (Million Baht) | Total (Million Baht)
2004 | 6,266 | 3,030 | 472 | 9,767
2005 | 8,878 | 3,117 | 264 | 12,259
2006 | 7,811 | 3,777 | 252 | 11,839
2007 | 9,036 | 3,573 | 290 | 12,899
2008 | 8,117 | 3,461 | 306 | 11,883
2009 | 8,102 | 4,474 | 467 | 13,043
2010 | 5,277 | 4,087 | 392 | 9,757
2011 | 9,489 | 4,154 | 842 | 14,484

## Slide 9: Marginal Cost – Expressway Section
Simple Cost Function
  Ln (Cost) = a + b Ln (Traffic Volume)
Panel Data – 10 Years – 3 Sections
+---------+--------------+----------------+--------+---------+----------+
|Variable | Coefficient | Standard Error |b/St.Er.|P[|Z|>z] | Mean of X|
+---------+--------------+----------------+--------+---------+----------+
VT 1.01283928 .20523989 4.935 .0000 17.6143412
Constant -1.63606367 3.61932223 -.452 .6512
R-squared = .5592385
MC (Infrastructure) = 1.0128 Average Cost

## Slide 10: Preliminary Results

## Slide 11: Data on Accident
 | 2011 | 2010 | 2009 | 2008 | 2007
Fatalities | 336 | 454 | 579 | 602 | 652
Seriously Injuries | 288 | 841 | 1,019 | 1,304 | 2,193
Minor Injuries | 7,416 | 13,109 | 17,073 | 19,448 | 20,293
No. of Accidents | 40,784 | 37,051 | 41,936 | 49,093 | 50,633
Property Damages (Baht) | 70,686,010 | 357,959,489 | 2,305,444,733 | 1,061,187,103 | 767,535,323
Bangkok | Average Accident Value (Baht/Case)
Fatalities | 6,190,590
Seriously Injuried | 253,098
Minor Injuried | 135,014
Property Damages | 127,693
The Study of Traffic Accident Cost in Thailand (2007)

## Slide 12: Accident Cost
 | 2011 | 2010 | 2009 | 2008 | 2007
Fatalities | 2,080 | 2,811 | 3,584 | 3,727 | 4,036
Seriously Injuries | 73 | 213 | 258 | 330 | 555
Minor Injuries | 1,001 | 1,770 | 2,305 | 2,626 | 2,740
Damaged cost | 5,208 | 4,731 | 5,355 | 6,269 | 6,465
Total | 8,362 | 9,524 | 11,502 | 12,951 | 13,797
In millions Baht

## Slide 13: Revenues
Fix Revenues
  Excise Duty on New Vehicles
  Annual Vehicle Tax
Variable Revenues
  Excise Duty on Fuel
  VAT on Fuel

## Slide 14: Fixed Revenues
Excise Duty on New Vehicles (Million Baht)
Annual Vehicle Tax (Million Baht)
 | 2011 | 2010 | 2009 | 2008 | 2007
Car | 9,054 | 8,335 | 7,714 | 7,338 | 7,030
Pick-up | 1,371 | 1,322 | 1,283 | 1,265 | 1,257
Taxi | 83 | 78 | 73 | 68 | 64
Motocycle | 520 | 495 | 475 | 466 | 451
Bus | 273 | 267 | 251 | 248 | 244
Truck | 1,534 | 1,459 | 1,476 | 1,472 | 1,425
Total | 12,835 | 11,956 | 11,272 | 10,857 | 10,470
 | 2011 | 2010 | 2009 | 2008 | 2007
Car | 22,229 | 25,272 | 21,426 | 35,363 | 42,623
Pick-up | 4,250 | 3,716 | 2,844 | 4,091 | 4,640
Motorcycle | 305 | 327 | 323 | 409 | 501
Total | 26,783 | 29,315 | 24,593 | 39,862 | 47,764

## Slide 15: Variable Revenues
QUANTITY (Thousand LITRES)
Consumption of Petroleum Products in Bangkok
Chart: 
| 2006 | 2007 | 2008 | 2009 | 2010 | 2011
ULG 95 | 679330.771 | 536825.7927 | 188462.7472 | 115472.9333 | 54038.7037 | 31333.9959
UGR 91 | 1435971.38 | 1452701.1108 | 1044829.2802 | 860200.208 | 926301.5678 | 967926.5202
Gasohol 95-E10 | 507524.172 | 633371.1964 | 1035677.5676 | 1227237.7177 | 1092331.6409 | 847843.2299
Gasohol 91-E10 | 63900.089 | 116993.8403 | 344844.8908 | 494482.5373 | 526977.9242 | 601251.9786
HSD | 5920152.043 | 6021752.1335 | 4048045.8395 | 2800029.7397 | 3303542.1373 | 5368320.2111
HSD B 5 | 16269.529 | 157004.7145 | 1228966.2848 | 2747040.0262 | 2375635.5692 | 213883.8889

## Slide 16
Chart: 
| 2006 | 2007 | 2008 | 2009 | 2010 | 2011
ULG 95 | 2503333.8911 | 1978203.0463 | 694485.2234 | 697177.8986 | 378270.9263 | 219337.9711
UGR 91 | 5291554.5353 | 5353203.5933 | 3850195.8977 | 4852389.9754 | 6484110.9743 | 6775485.6413
Gasohol 95-E10 | 1683203.9164 | 2100575.573 | 1756138.2315 | 6056631.7034 | 6881689.3376 | 5341412.3484
Gasohol 91-E10 | 211924.6452 | 388010.0713 | 506720.6479 | 2454023.8864 | 3319960.9226 | 3787887.4652
HSD | 12889257.0321 | 13880138.6676 | 5455453.1709 | 11854607.6743 | 17541808.7492 | 8024187.3869
HSD B5 | 35627.0146 | 343808.9238 | 1059776.0184 | 10272583.8119 | 11973203.269 | 1077974.7999
Excise Duty of Petroleum Products in Bangkok
QUANTITY (Thousand Baht)

## Slide 17: Variable Revenues
Year | Excise Duty (Million Baht) | VAT (Million Baht) | Total (Million Baht)
2006 | 22,615 | 11,056 | 33,671
2007 | 24,044 | 11,674 | 35,718
2008 | 13,323 | 13,197 | 26,519
2009 | 36,187 | 9,150 | 45,337
2010 | 46,579 | 10,825 | 57,404
2011 | 25,226 | 13,701 | 38,927

## Slide 18: On Average …
 | 2011 | 2010 | 2009 | 2008 | 2007
Infrastructure Cost | 14,484 | 9,757 | 13,043 | 11,883 | 12,899
Accident Cost | 8,362 | 9,524 | 11,502 | 12,951 | 13,797
Total Cost | 22,846 | 19,281 | 24,545 | 24,834 | 26,696
Fixed Revenues | 39,618 | 41,271 | 35,865 | 50,719 | 58,234
Variable Revenues | 38,927 | 57,404 | 45,337 | 26,519 | 35,718
Variable Revenue/Cost Ratio | 1.704 | 2.977 | 1.847 | 1.068 | 1.338
Total Revenue/Cost Ratio | 3.438 | 5.118 | 3.308 | 3.110 | 3.519
In the Missing of
Environment Cost / Congestion Cost (MC)
Results Suggested
Accident Cost is significant for the Revenue/Cost Ratio

## Slide 19: Conclusions
This research presents the concept of marginal social cost in road transport
In order to calculate the marginal cost, longitudinal and detailed data is a necessity.
Due to lack of data, we are able to calculate only (roughly) marginal infrastructure cost.
However, we use the average accident cost as a proxy to the marginal cost.
We then compare the costs and revenues in Bangkok area.

## Slide 20: Remarks
The policy of the excise duty on various fuel types may not consistent with the social cost occurred.
For Future Research:
This topic should be further developed in more detail in many issues, including the marginal accident cost.
Furthermore, the congestion cost should also be discussed, though it will be very difficult.