## Slide 1: A Development of Motorcycle On-road Emissions and Fuel Consumption Models for a Traffic Simulation
By
Thaned Satiennam
17 August 2012
Final Report Presentation
Project No - 11-12/004
Notes: Good afternoon, lady and gentlemen, Today, let me share with you my current and interesting research entitle “A development of Motorcycle on-road exhaust emission models for a traffic simulation”
This topic, I and my research team got an aspiration from Prof. Barth and Prof. Fukuda.
Our research team has done this research with cooperation with the Pollution Control Department of Thailand. And, last but not least, this research has been fund continuously by ATRANS.

## Slide 2: Research Team
Dr.Thaned Satiennam, KKU
Dr.Thana Radpukdee, KKU
Dr.Ittiphol Pawarmart, PCD
Mr.Hashino Yoshihiko, PTV-Japan
Mr.Watcharain Saengsuwan, Zen-microtech
Mr.Atthapol Seedam, KKU
Notes: At first, let me outline my presentation that start from introduction of this research, and how to develop the onboard measuring system, then validation of gas analyzer, collecting on-road data at a study city, my hometown, Khon Kaen city. After that developing driving cycle, then developing emission factor and emission rate.
Finally, how to apply the developed emission factor and emission rate to estimate the vehicle emissions through the transportation models

## Slide 3: Presentation Outline
Introduction
Onboard Measuring System Development
Validation of Gas Analyzer
On-road Data Collection at Khon Kaen City
Driving Cycle Development
Emission Factor and Emission Rate Development
Fuel Consumption Model Development
Application of Developed Emission and Fuel Consumption models
Conclusion and Upcoming Studies
Notes: At first, let me outline my presentation that start from introduction of this research, and how to develop the onboard measuring system, then validation of gas analyzer, collecting on-road data at a study city, my hometown, Khon Kaen city. After that developing driving cycle, then developing emission factor and emission rate.
Finally, how to apply the developed emission factor and emission rate to estimate the vehicle emissions through the transportation models

## Slide 4
Motorcycle has become a popular mode in many Asian cities with its high accessibility.
A private vehicle for almost low-income households due to cheap and advantage for a short distance travel in the congested cities.
However, MC recorded as highest mode violated traffic rules and involved in traffic accidents.
To alleviate this problem, appropriate traffic management and control concerning with MC necessary rather than traffic rule education and traffic law enforcement.
To evaluate traffic control strategy in term of emission and fuel consumption reduction, estimation of on-road emissions and fuel consumption by traffic simulation is necessary.
It requires emission and fuel consumption models sensitive to instantaneous speed profile of MC
Existing driving cycle of MC may not be a good representative for driving cycle of other cities
Introduction
Notes: background to my research, this research focuses to study the driving pattern and exhaust emission of motorcycle.
As you know that it is a popular mode in many Asian cities with its high accessibility
It becomes a private vehicle for low-income households
However, motorcycle recorded as highest mode violated traffic rules and involved in traffic accidents.
To lesson this problem, appropriate traffic management and control concerning MC necessary rather than traffic law enforcement and traffic rule education
To evaluate these strategies in term of emission reduction, estimation of on-road emissions by traffic simulation is necessary.
To do that, emission model sensitive to instantaneous speed profile of MC is neccessary

## Slide 5
Application Parts
Development Parts
Research Scope
Development of Mobile Measurement System
Highway
City road
Dense intersection road
On-road Data Collection on selected roads
Development of Driving Cycle, Emission Factor, Emission Rate
Evaluation of Proposing Traffic Management Policy
Study Section
Data Collection on
Selected road section
Traffic Simulation Model Development

## Slide 6: Mobile Measuring System Development
SD Card
GPS module
Microcontroller
Validation requirement
Validation requirement
Fuel flow sensor
Carburetor
Calibrated
Notes: First step, we developed the equipment that could be installed on the motorcycle driving on the road to collect instantaneous exhaust emissions in according to speed profile
The developed equipment consists of gas analyzer that can measure instantaneously exhaust emissions, including CO CO2 HC and Nox
Speed sensor installed at the rear wheel to measure speed profile of MC
And the data logger, it receive the transfer data from measuring units and record into memory unit by every second

## Slide 7
Validation Methodology
1. Simulating a gasoline engine in accordance with ECE and Bangkok driving cycle
2. Instantaneous measuring exhaust emissions of gasoline engine by both Exhaust Emission Dynamometer of PCD and a gas analyzer
3. Comparison measured results by statistical testing
4. Developing adjusted equation for correcting the exhaust emissions measured by a gas analyzer
Exhaust Emission Dynamometer of PCD
Calibration with Gas Standard every time
Measurement by smaller scale
Control temperature and humemity
Gas Analyzer of KKU
Calibration by manufacturer
Validation of Gas Analyzer at PCD
Validation processed at Automotive Emission Laboratory of Pollution Control Department
Driving following driving cycle
Stimulating Loads
Directly measuring
Exhaust Emissions
Notes: After we developed the equipment, we need to validate our gas analyzer at Automotive Emission Laboratory of Pollution Control Department
To do that, we simulated the gasoline engine in accordance with ECE driving cycle and measure instantaneously the exhaust emissions measured by our gas analyzer and Exhaust Emission Dynamometer of PCD. Then making a comparison of both measurement results.

## Slide 8
Results of Measuring Exhaust Emissions in Laboratory
Chart: 
Chart: 
Chart: 
Notes: These graphs, showing results of comparison.
The black line presents driving cycle or speed pattern
The blue line presents emissions measured by Exhaust Emissions dynamometer of PCD
The red line presents emission measured by a gas analyzer of KKU
The results show that trend of KKU line matching with those lines of PCD.
However, we still notice the amount of emissions measured by our gas analyzer somehow higher than those measured by equipment of PCD
We think that it causes from the difference in scale of measurement. So, we need such a equation to adjust our measured exhaust emission

## Slide 9
Results of Gas Analyzer Validation (2)
Chart: 
Trend of graphs of emissions measured by KKU gas analyzer quite matched with those of PCD Exhaust Emission Dynamometer
NOx measured by KKU gas analyzer high relative with those measured by Exhaust Emission Dynamometer, Not required adjustment
CO measured by KKU gas analyzer required the adjusted equation to correct with those of Exhaust Emission Dynamometer
Adjusted Exhaust Emission Equations | R2 | Remark
COPCD = - 0.00002COKKU2 + 0.6566COKKU + 22.768 | 0.90 | Acceptable
NOx PCD = 0.4595NOx KKU - 0.4724 | 0.98 | Not Required Adjustment
Validation Conclusion
Chart: 
Notes: This slide show results of developing of validation equation by linear regression
These equations will be used to adjust the emission measured from our gas analyzer

## Slide 10
Chart: 
Fuel Consumption in according to Speed Profile

## Slide 11
On-road Data Collection at Khon Kaen City
Highway
City road
Dense intersection road
Khon Kaen City selected as a study city with motorcycle 30% of mode share
It locates in the Northeast part of Thailand
The onboard measurement system was installed on the motorcycle to drive on the Khon Kaen road network
To measure the driving pattern and exhaust emissions by road type.
The road network of Khon Kaen city was classified into three road types, including Highway, Urban road and dense signalized intersection road (Idle mode).
The driving data was collected during the morning peak hour between 7:00 a.m. to 9:00 a.m. in a weekdays and weekend conditions for 2 months.
Selected Routes on KKC Road Network
MC Driving on Road for Data Collection
Notes: After we developing the equipment, we decided to install it on the motorcycle to collect its driving pattern and exhaust emission at a
Khon Kaen city for data collection since its another major city that have a high motorcycle mode share.
We classified the KK road network into Highway, urban road and dense signalized intersection road
The driving data was collected during peak hour on everyday for several months.

## Slide 12
Tracking Emissions and Fuel Consumption in accordance with Speed Profile along the existing road

## Slide 13: Development of Driving Cycle for Motorcycle in KKC
Target Parameters | Khon Kaen Motorcycle Driving Cycle (KMDC) | Bangkok Driving Cycle (BDC) | European Driving Cycle (ECE) | Taiwan Motorcycle Driving Cycle (TMDC)
Vavg, km/h | 24.97 | 17.4 (-30.3%) | 33.4 (33.8%) | 16.62 (-33.4%)
V1avg, km/h | 31.84 | 28.1 (-11.8%) | 44.4 (39.4%) | 23.66 (-25.7%)
Accavg, m/s2 | 0.636 | 0.71 (11.6%) | 0.541 (-14.9%) | 0.68 (6.9%)
Decavg, m/s2 | -0.692 | -0.71 (-2.6%) | -0.789 (-14%) | -0.68 (1.7%)
%Idle | 20.8 | 37.7 (81.3%) | 23.7 (13.9%) | 30 (44.2%)
%Cruise | 17.83 | 23.7 (32.9%) | 42.2 (136.7%) | 22 (23.4%)
%Acc. | 31.97 | 15.2 (-52.5%) | 18.3 (-42.8%) | 24 (-24.9%)
%Dec. | 29.4 | 23.4 (-20.4%) | 15.8 (-46.3%) | 24 (-18.4%)
PKE, m/s | 0.448 | 0.45 (-0.4%) | 0.224 (-50.0%) | -
Start
Identify speed-time data to micro-trips
Arrange micro-trips into 5 speed ranges indentified by i (0 < i < 5)
Calculate time fraction of micro-trips and idle time
Randomly select micro-trip from the selected speed range i
Collect speed-time data from on-road driving
Connect the micro-trip to the previous micro-trip (if exist)
No
Yes
Average error is less than the pre-defined threshold (≤ 4%)?
Stop
Calculate the 9 target parameters from the collected speed-time database
Calculate the average error of 9 target parameters
Calculate the 9 target parameters from the constructed driving cycle
Select initial speed range from database (at i =1, 2, 3, 4, 5)
Insert the idle time into the micro-trip
Calculate total time of the connected micro-trips
Calculate maximum time of micro-trip in speed range i
No
Initial define duration of cycle time (1,200 sec.)
Yes
Change speed range
Total time of connected micro-trips is less than maximum time of micro-trip in speed range i?
Decrease average error?
Algorithm for Driving Cycle Development
Comparison of developed driving cycle with other driving cycles
Developed driving cycle for MC in KKC
Vmax= 63 km/h; Accmax= 2.778 m/s2; Decmax= -2.787 m/s2; length = 1,164 s; distance= 8.113km
Driving cycle of MC in KKC is rather different from the driving cycles of Bangkok and other cities.
Notes: After we got the data, I would like to show how we use those data to develop driving cycle.
For developing driving cycle, we applied such statistic way to develop a driving cycle that should be a good representative of all driving data
We got driving cycle of MC in KKC, when we compared with existing driving cycles of other cities. It means that each city should have their own driving cycle. If you want to further use to develop emission factors to estimate emission appropriately.

## Slide 14: Emission Factors and Emission Rates Development
Emissions Rate of MC | R2
(EMRCO)(g/s) = 0.101- 0.002u (km/hr) + 0.449a (m/s2) | 0.571
(EMRCO2)(g/s) = 0.269 + 0.005u (km/hr) - 0.548a (m/s2) | 0.961
(EMRHC)(g/s)= 0.005 - 0.00099u (km/hr) + 0.014a (m/s2) | 0.811
(EMRNOx)(g/s)= - 0.001 + 0.00088u (km/hr) - 0.015a (m/s2) | 0.931
Where as
EMR = Emission Rate, g/s
u = Instantaneous Speed, kph
a = Acceleration Rate, m/s2
Notes: Also from those collected data, we can use to develop the emission factor (indicating amount of exhaust emissions, gram per kilometer in according to aver. speed) as well as emission rate model (indicating amount of emissions, gram per second, in according to instantaneous speed and acceleration rate).

## Slide 15: Fuel Consumption Factor and Rate Development
Fuel Consumption rate model | R2
(FRCO)(ml/s) = 0.131 + 0.0001u (km/hr) + 0.959a (m/s2) | 0.963
Where as
FR = Fuel Rate, ml/s
u = Instantaneous Speed, kph
a = Acceleration Rate, m/s2
Notes: Also from those collected data, we can use to develop the emission factor (indicating amount of exhaust emissions, gram per kilometer in according to aver. speed) as well as emission rate model (indicating amount of emissions, gram per second, in according to instantaneous speed and acceleration rate).

## Slide 16: Conclusion and Next-step Research
Development of Eco-driving cycle
Automatic Eco driving Behavior Guide system in motorcycle for Reduction of Emission and Fuel consumption
Green On = Eco Driving mode
Red On (Right) = Over limit
Red On (Left) = Under limit
Eco-driving assistance monitor
Next-step Research
Conclusion
Mobile on-board emissions and fuel consumption measuring system was developed
On-board emissions and fuel consumption models were developed

## Slide 17: Thank you for your kind attention
17